## Slide 1: Designing a Sustainable Model for Financial Viability of Decentralized Bio-fuel based Power Projects
Debajit Palit & Ramit Malhotra
The Energy & Resources Institute, New Delhi

## Slide 2: Acknowledgement
The OASYS Project Objectives:
Are there cost-effective and reliable off-grid electricity supply solutions that can meet the present & future needs, are socially acceptable, institutionally viable and environmentally desirable?
Do these local solutions have the scaling-up and replication potentials and can these solutions be brought to the mainstream for wider electricity access in the developing world?
www.oasyssouthasia.info

## Slide 3: Electricity Situation in India
India is one of the fastest growing economies;
While 94% of the villages are electrified, around 290 million people still without access;
  93.83% of total urban households are electrified
  65.61% of total rural households have access
In 2001, Government of India declared the objective of ‘Power for All by 2012’;
Launched REST Mission in 2011, RGGVY in 2005, RVE in 2001 and VESP in 2004;
Chronic shortage of electricity supply

## Slide 4: Bio fuel program in India
  India initiated biofuel production nearly a decade ago to reduce its dependence on foreign oil and improve energy security;
    Launched National Mission on Biodiesel in 2003;
    Program was mainly directed towards using the fuel as transport fuel;
    Straight Vegetable Oils also are promising candidates for small scale power generation in rural areas;
    VESP used SVO for power generation for remote villages;
  We are focusing here on experience and learnings from biofuel based power generation in the remote areas

## Slide 5: Village Energy Security Program (VESP)
Aim was to provide total energy security at the village level, through locally available resources like biomass, with full participation and ownership of community
Technologies used
  Biomass gasifier
  Bio fuel engines
  Improved cookstoves
  Biogas
  Energy Plantation

## Slide 6: Some glimpses

## Slide 7: Research Objectives
Design a sustainable model for financial viability of SVO based power projects
Analysis from the perspective of all key stakeholders:
  Project Implementing Agency - evaluate the techno-economic viability of SVO system based mini-grids to provide rural electricity services
  Government - assess the financial burden of subsidies for making electricity affordable as compared to extending the central grid for rural electrification
  Consumers - tariff within the payment capacity for availing the electricity services

## Slide 8: Possible mode of financing
Possible financing
Without subsidy
With 90 % subsidy
30 % Equity
70 % Debt
10% equity from PIA or community
10 % grant from state department

## Slide 9: Methods
Estimation of Minimum Desired Price (MDP) of electricity under different operating conditions for ensuring viability of SVO systems
  Based on actual field performance data collected from a number of projects implemented under VESP
Finding MDP from a consumer’s perspective and viability gap analysis to estimate any gap
Possible mechanisms to bridge the gap and suggest breakeven price under different scenarios
Suggests an integrated approach for ensuring long term ‘sustainable electrification’ with SVO systems as an option in the remote rural areas

## Slide 10: Input parameters
Particulars | Unit | SVO system
Capacity of engine generator | kWe | 10
Capacity of oil expeller | Litres/hour | 10
Life of distribution network | Years | 30
Average load (of rated capacity) | % | 40
Hours of operation per day | hours | 4
Distribution line network (average) | Km | 2
Specific Fuel Consumption | Litres/kWh | 0.35
Auxiliary consumption & technical loss | % | 5
System cost (in thousands) | INR | 375
Civil Shed (in thousands) | INR | 200
Cost of PDN (in thousands ) | INR/km | 150
Interest rate on loan | % | 11.25
Fuel (seed) cost | INR/kg | 6.00
Annual O&M cost (1st year) | INR | 42000
Annual escalation in O&M & fuel cost | % | 5
Discount rate | % | 12

## Slide 11: MDP from a SVO system
 | Without subsidy | With 90% subsidy
Rated capacity (kWe) | 10.00 | 10.00
MDP (INR/kWh) | 17.89 | 11.31
MDP (INR/kWh) | 12.53 | 10.77
CUF | MDP (INR/kWh) for 10 kWe SVO system
7% (Av 40% load) | 19.79
13% (Av 40% load) | 14.82
20% (Av 80% load) | 12.79
25% (Av 80% load) | 12.04
33% (Av 80% load ) | 11.31
based on 33% CUF; $1 = INR 50

## Slide 12: Sensitivity analysis

## Slide 13: Required Tariff
Scenario load (in kW) | Dom -3 Com - 5
AV Load (kW) | 8
MDP INR/kWh | 14.67
Consumption - Dom (kWh/month), 4 h/d | 360
Consumption - Com (kWh/month) , 4 h/d | 600
Required Tariff - Dom (INR/month) | 50.00
Income from Oil cakes (INR) | 960
Required tariff - Com (INR/kWH) | 15.2
$1 = INR 50

## Slide 14: Effect of Productive Load
SVO based project will be economically viable if proposed commercial tariff is set at around INR15/kWh
Local micro-enterprises such as rice hauler may be reluctant to pay such high tariff, as it may not reduce their current expenses as compared to diesel

## Slide 15: Integrated oil expeller - biogas system
Integrated SVO oil expeller-biogas system could be solution
  Oil extracted using mechanical oil expeller is sold at market prices in the local market
  Residual oil cakes are used as fuel in biogas digester
  De-oiled cake price say @ INR 1/kg, gas production of 0.5m3/kg cake, & power generation of 1 kWh per m3 will result in
  Unit cost of electricity generation ~ around INR 4 per kWh

## Slide 16: In Conclusion
The model has huge potential to generate employment through biofuel plantation and processing to enhance local income and at the same tome generate electricity to serve the same area
Ecosystem
Appropriate Technology
Innovative Financing
Local Skills
Enabling Policy
Sustainability condition